## Slide 1: Automated Variance Reduction for SCALE Shielding Calculations
Douglas E. Peplow
and John C. Wagner
Nuclear Science and Technology Division
Oak Ridge National Laboratory
14th Biennial Topical Meeting of the ANS
Radiation Protection and Shielding Division
April 3-6, 2006
Carlsbad, New Mexico, USA

## Slide 2: Motivation
Codes need to solve increasingly difficult problems
Need accurate and fast answers
Monte Carlo with importance sampling is the best variance reduction
Codes need to be simple and as automated as possible

## Slide 3: Background
SCALE (Standardized Computer Analyses for Licensing Evaluation)
  Collection of codes for performing criticality safety, radiation shielding, spent fuel characterization and heat transfer analyses
  Control modules or sequences automate the execution and data exchange of individual codes to perform various types of analyses
SAS4 – Shielding Analysis Sequence
  Automated 1-D variance reduction capability for more than a decade, with limitations
  Effective for cask midplane and top center dose
  Not well suited to cask corners and very heterogeneous geometries
  Hence, need for Monte Carlo tool with automated 3-D variance reduction (AVR) for general shielding applications

## Slide 4: CADIS Methodology - Consistent Adjoint Driven Importance Sampling
Use Discrete Ordinates to find approximate adjoint flux
From the adjoint flux
  Importance map for MC transport (weight windows for splitting and roulette)
  Biased source distribution
Biased source and importance map work together

## Slide 5: SCALE Implementation of CADIS
Cross sections
  Multi-group SCALE libraries – many choices
  Create adjoint and forward cross section sets
Find the approximate adjoint flux
  GRTUNCL3-D – first collision code
  TORT – three dimensional DO transport code
Monaco
  Descendant of MORSE – still in progress
  Uses SCALE general geometry (KENOVI)
Automate as much as possible

## Slide 6: SCALE Sequence: MAVRIC
Monaco with Automated Variance Reduction using Importance Calculations
SCALE
Driver
and
MAVRIC
Input
ICE
Monaco
End
Optional: TORT adjoint cross sections
Optional: 3-D discrete ordinates calculation
3-D Monte Carlo
Resonance cross-section
processing
BONAMI / NITAWL or
BONAMI / CENTRM / PMC
TORT
GRTUNCL-3D
Optional: first-collision source calculation

## Slide 7: SCALE Sequence: MAVRIC
Monaco with Automated Variance Reduction using Importance Calculations
Input:
  Physical Problem
    Materials
    Geometry
    Source
    Det. Positions
    Det. Responses
  Monte Carlo info
    Histories, max time, etc
  Adjoint DO info
    Adjoint source
    Spacial discretization

## Slide 8: Example
Simple cask with ventports
Spent fuel:
  UO2 (20%), air
  Uniform source
Steel, Concrete

## Slide 9: Example
Source: photons
Response: photon dose

## Slide 10: Analog Monaco

## Slide 11: Example - Discretization

## Slide 12: Example – Adjoint Flux

## Slide 13: Example – Imp. Map/Biased Source

## Slide 14: Example – Biased source distribution

## Slide 15: Results

## Slide 16: Results
Compare MAVRIC and Analog

## Slide 17: Results
Compare MAVRIC and SAS4

## Slide 18: Results
Compare MAVRIC and others: FOM ratios to analog Monaco

## Slide 19: Results
Compare MAVRIC and ADVANTG: FOM ratios to analog

## Slide 20: Future Work
MAVRIC Sequence
  Automatic homogenization in importance map
  Determine standard set of TORT parameters
Monaco
  Flux tallies for regions
  Mesh tally
Testing, Testing, then a bit more Testing

## Slide 21: Discussion & Questions