## Slide 1: PENTRAN -CRT Problem Exercises
AFIT Workshop
October 2015

## Slide 2: Parallel Job Processing
2
Two Modes for Execution: Interactive or Batch
  Interactive Mode
    Interesting for debug, poor use of system
    Scripts available
  Batch Mode (e.g. PBS scheduler)
    Allocates jobs to least used cores automatically
  Scripts for pre- and post- parallel PENTRAN
    ppen.post prbname pen #n #c
    ppen.pre prbname pen #n #c
  Post processing with PENDATA, PENMSHXP
Notes: PENTRAN CODE SYSTEM
2

## Slide 3: Sample Reactor Problem: zippy
3
Zippy reactor problem
  6x6 Coarse Mesh problem with control rod /water flux traps
    zippy.pen
    Water(m2)
    Fuel (m1)
    Water or Control Rod (m3)
    Reflective
Notes: PENTRAN CODE SYSTEM
3

## Slide 4: Sample Shielding Problem: pbshield
4
pbshield shielding problem 10x10x10 cm
~100,000 meshes, S12P1, 2G
  3x3x3 Coarse Meshes,
    pbshield.pen
    Pb
    Water
    10 Ci CsCl
    Stainless steel
    Reflective
Notes: PENTRAN CODE SYSTEM
4

## Slide 5: Sample Shielding Problem: pbshield
5
pbshield shielding problem 10x10x10 cm
~100,000 meshes, S12P1, 2G
  3x3x3 Coarse Meshes,
    pbshield.pen
    10 Ci CsCl
    Water
    Pb
    Stainless steel
    Reflective
Notes: PENTRAN CODE SYSTEM
5

## Slide 6: Run zippy.pen
6
Prepare a 2 Parallel core Script for zippy.pen
  Prefix: zippy Suffix: pen Nodes 1 Cores: 2
  pen.pre zippy pen 1 2
    Copies zippy.pen to prb.pen
    Sets up script to execute
  Submit to queue—script needed
Post process output: ppen.post zippy pen 1 2
Notes: PENTRAN CODE SYSTEM
6

## Slide 7: PENDATA Procedure
7
PENDATA
  Data (to the highest degree possible) is stored in PENTRAN as PARALLEL memory—each processor contains data only LOCALLY
  If requested, outputs will be in a number of files
    zippy.1, zippy.2 … run output from proc. 1, 2, etc
      Contains important run data and metrics
    zipply.L1, zippy.L2 … logfile outputs, etc
    zippy.f1, zippy.f2 … binary flux data, etc
    zippy.j1, zippy.j2 … flux and net current, etc
Notes: PENTRAN CODE SYSTEM
7

## Slide 8: Run PENDATA, PENMSH-XP Plot
8
To run PENDATA
  In the local problem directory, type PENDATA <enter>
    Enter the options as desired
    PENDATA will gather all files from the parallel run in a transparent manner
To use PENMSH to plot:
  Go to crit directory
  Type penmsh –i moddir –f flxdir -msf 4
    Will reference model and run to plot fluxes
Notes: PENTRAN CODE SYSTEM
8