## Slide 1: PENTRAN -CRT Problem Exercises
Colorado School of Mines
PENTRAN-CRT Workshop
March 2014

## Slide 2: Parallel Job Processing
2
Two Modes for Execution: Interactive or Batch
  Interactive Mode
    Interesting for debug, poor use of system
  Batch Mode in IBM Blue Gene
    “sbatch” Batch Scheduler by IBM
      Job “squeue” for Queue core use
      Allocates jobs to least used cores automatically
    Scripts for pre- and post- parallel PENTRAN
      mpisub ppencrt prbname pen #n #c, ppen-post prbname pen #n #c
    Post processing with PENDATA, PENMSH
Notes: PENTRAN CODE SYSTEM
2

## Slide 3: Sample Reactor Problem: zippy
3
Zippy reactor problem
  6x6 Coarse Mesh problem with control rod /water flux traps
    zippy.pen
    Water(m2)
    Fuel (m1)
    Water or Control Rod (m3)
    Reflective
Notes: PENTRAN CODE SYSTEM
3

## Slide 4: Sample Shielding Problem: pbshield
4
pbshield shielding problem 10x10x10 cm
~100,000 meshes, S12P1, 2G
  3x3x3 Coarse Meshes,
    pbshield.pen
    Pb
    Water
    10 Ci CsCl
    Stainless steel
    Reflective
Notes: PENTRAN CODE SYSTEM
4

## Slide 5: Sample Shielding Problem: pbshield
5
pbshield shielding problem 10x10x10 cm
~100,000 meshes, S12P1, 2G
  3x3x3 Coarse Meshes,
    pbshield.pen
    10 Ci CsCl
    Water
    Pb
    Stainless steel
    Reflective
Notes: PENTRAN CODE SYSTEM
5

## Slide 6: Run zippy.pen
6
Prepare a 2 Parallel core Script for zippy.pen
  Prefix: zippy Suffix: pen Nodes 1 Cores: 2
  mpisub ppencrt zippy pen 1 2
    Copies zippy.pen to prb.pen
    Sets up zippy.scr script
  Submit to queue: sbatch zippy_2_pbs.scr
    Note the job number reported back
    Check queue status: squeue <enter>
      When in workdir, type “peek” to see parallel feedback of last submitted job
Post process output: ppen-post zippy pen 1 2
  To Prepare Batch Mode via PBS
    ppen-pre zippy pen 2
Notes: PENTRAN CODE SYSTEM
6

## Slide 7: PENDATA Procedure
7
PENDATA
  Data (to the highest degree possible) is stored in PENTRAN as PARALLEL memory—each processor contains data only LOCALLY
  If requested, outputs will be in a number of files
    zippy.1, zippy.2 … run output from proc. 1, 2, etc
      Contains important run data and metrics
    zipply.L1, zippy.L2 … logfile outputs, etc
    zippy.f1, zippy.f2 … binary flux data, etc
    zippy.j1, zippy.j2 … flux and net current, etc
Notes: PENTRAN CODE SYSTEM
7

## Slide 8: Run PENDATA, PENMSH-XP Plot
8
To run PENDATA
  In the local problem directory, type PENDATA <enter>
    Enter the options as desired
    PENDATA will gather all files from the parallel run in a transparent manner
To use PENMSH to plot:
  Go to crit directory
  Type penmsh –i moddir –f flxdir -msf 4
    Will reference model and run to plot fluxes
Notes: PENTRAN CODE SYSTEM
8