## Slide 1: PENTRAN-CRT Code Workshop
AFIT
October 2015

## Slide 2: Overview
2
Code Overview – G. Sjoden
  Features, Adaptive Differencing, Parallel Issues
Code Examples and Applications –
Large problems, Hybrid Methods, etc
  Parallel Performance
Problem examples
  Parallel Scripts, PENDATA gathering
  Output Details and analysis tools
PENMSH-XP
Problem and Mesh Generation Tools
PENMSH-XP GUI
Exercises and Exploration
Notes: PENTRAN CODE SYSTEM
2

## Slide 3
Presented by
Glenn E. Sjoden, Ph.D., P.E.
PENTRAN Code Overview

## Slide 4: PENTRAN Code Update
4
To be available Free to Universities via RSICC at ORNL
  http://www-rsicc.ornl.gov/
  US Citizens and US Residents
PENTRAN runs on ALL types of distributed parallel computers
  Parallel decomposition in Angle, Energy, and Space
  ANSI F90 standard code
  Tested on up to 4096 Cores with excellent scaling
  Has undergone significant benchmarking
  Is under continuous enhancement
Training is available
In cooperative development between HSW Technologies LLC and Georgia Tech/NRE
Notes: PENTRAN CODE SYSTEM
4

## Slide 5: PENTRAN Parallel Code System
PENMSHxp -- “PENMSH eXPress” by C. Yi and A. Haghighat
  Automatic mesh and code deck generation
“PENTRAN-CRT” Code with adaptive Sn and Characteistic Ray Trace Hybrid
  Now Undergoing testing and benchmarking with TITAN code
“PENTRAN-MP” Code Set for Whole Body Medical Physics Applications
  Under further development and testing with Electron Dose Kernel (EDK) Methodology
“PENBURN” Burnup Module for 3-D burnup/parallel chain processing
Used for new methods in detection, characterization, reactor analysis
Scalable memory & processing enables ‘extreme’ transport to >109 unknowns
5
Notes: PENTRAN CODE SYSTEM
5

## Slide 6: PENTRAN Overview
Parallel Computing & MPI
Boltzmann & Sn Transport
PENTRANTM Code System
Features
  Adaptive Differencing, Parallel
Discussion and Summary
Questions

## Slide 7: What is Parallel Computing?
Computer with many processors
  “Lumped” or Network “Distributed”
  Divide problem up on processors
Serial...
  Task1
  Task2
  Task3
  RESULT
Parallel…
Task1 Task2 Task3
RESULT

## Slide 8
About MPI...
MPI (Message Passing Interface) Library
Began with “MPI Vendor Forum” May 1994
      Formalized in 1995
    For distributed memory machines (FORTRAN, C, other language variants support)
    ANSI-like “standard” in message passing
    Process com groups, decomposition topologies
    Port code directly to architectures running MPI
    Versions: MPICH, MPICH2, OPENMPI

## Slide 9
About MPI… (2)
A Minimum Set of MPI Calls (Fortran or C):

## Slide 10
Parallel Job Setup/Compile
Normal FORTRAN or C programming
MPI libraries are included in each routine requiring them:
  INCLUDE 'mpif.h’, include ‘mpi.h’
Same code executed on each processor
Logical coding controls "who does what"
User responsible for:
  start/stop/all synchronization
  message passing calls/memory management

## Slide 11
Amdahl’s Law: Speedup is Limited
  (Parallel Code Fraction = f )
  Sp = 1 / ((1-f) + f/p + Tc /Ts)
  Speedup= Sp = Ts / Tp, Efficiency= E = Sp / P
  If f =0.8, then max Sp =5.0 as P->Infinity

## Slide 12
Boltzmann Transport Equation
Track particles traveling in different …
    directions
    over a range of energies
    in different spatial locations in 3-D
3-D Boltzmann Equation

## Slide 13: Transport Theory
Boltzmann transport methods
  Monte Carlo method
  Discrete Ordinates (SN ) method
  Each has specific … Advantages (+) Disadvantages (-) Issues
Both methods can take advantage of
parallel processing!

## Slide 14
Balance Equation… “out” “in”
Surface Averaged Fluxes
3-D Discrete Ordinates (Sn)

## Slide 15: Monte Carlo
Advantages
  Traditional, straight forward
  Geometrically precise
  Robust particle physics--Continuous-Energy xsec
  Parallelization obvious: particle histories
Disadvantages:
  Processing time, Non-analog variance reduction
  Inevitable uncertainties and Central LT
  “Global” solution difficult to obtain
  Results can be limited in application

## Slide 16: Discrete Ordinates
Advantages
  Model entire geometry
  Fast and accurate
  Global flux distribution
  Directly allows for burnup, etc
Disadvantages:
  Proper multi-group cross sections
  Geometry discretized
  Memory, storage, differencing scheme issues
  Parallelization--coupling in angle, energy, space

## Slide 17
Parallel Environment Neutral-particle TRANsport
  Two decades of continuous development
    Introduced in 1996 by Sjoden and Haghighat
    Parallel SN in angle, energy, and space & I/O
    ANSI FORTRAN 90, ~40k lines
    Industry standard FIDO input
  Solves 3-D Cartesian Sn Equations
    Multigroup, anisotropic transport problems
  Forward and adjoint mode
    Fixed source
    Criticality eigenvalue problems
PENTRAN Code System

## Slide 18
Distributed Memory Programming Philosophy PENTRAN
Programming Model:
  View message passing as a last resort
    Minimize serialization, minimize barriers
  Use a partitioned memory storage of data
    Only way to solve larger problems
    Process mapping arrays to determine “who’s where”
Overall...
  Use of a coarse-grained code structure
  Many flops performed before messages passed
  Don’t forget about Amdahl’s Law

## Slide 19: Coarse Mesh/Fine Mesh Scheme
3 x 3 x 3 coarse mesh Model
Primary Two level meshing scheme for
Cartesian geometry
Model divided into coarse meshes (CMs)
  Each CM filled with fine mesh grids
  “Block adaptive” fine mesh structure,
  No requirements on surrounding CMs; Higher order coupling with TPMC
Intermediate mesh level (“medium” grids ) for “/-multigrid” nested iteration

## Slide 20: Block Adaptive Mesh Generation
PENMESH-XP- automatically sets up problem
  You define shapes, 3-D intervals, it does the rest…
  Coarse Mesh Structure
  Fully discontinuous variable meshing among coarse meshes

## Slide 21: PENMSH-XP input: “Z-level” basis
File names | Description | PENMSH XP
penmsh.inp | Meshing parameters | Required
prbname#.inp | Meshing per ‘z level’ | Required
prbname.src | Fixed source grid | Optional
prbname.spc | Source spectrum | Optional
prbname.chi | Fission spectrum | Optional
prbname.mba | Material balance | Optional
prbname#.flx or prb#.flx or .fjn files | Group fluxes (.flx) or current (.fjn) generated by PENDATA from PENTRAN calculation | Optional

## Slide 22
Sample Geometry Slice from PENMSH-XP
2-D Geometry, Flux Plots, nuclear reactor model

## Slide 23
Uses MPI Message Passing Interface library
Performs all I/O in parallel by each processor
Uses a local, partitioned memory for memory intensive arrays (angular fluxes, etc)
Memory Tuning feature for optimum memory use
Automatic scheduling based on a user-specified parallel decomposition weighting vector
Optimized Processor MPI “Communicators”
  Minimized messages, comm. processor “planes”
Adaptive Differencing
PENTRAN
Parallel Implementation

## Slide 24
PENTRAN 3-D model of fuel storage cask, 1/4 symmetry, 40 Group P3-S12, 318,426 cells : 2.14 Billion Eqns
Memory Tuning Example:
Fuel Cask Model

## Slide 25: Cask 3-D Flux Distribution
Group 1
Group 22
By Shedlock & Haghighat

## Slide 26
Original ISFSI Cask Model global upper limit memory specification wasteful
Optimized Memory Tuning Cask Model with Two-Level memory specification
Two-Level Memory Tuning

## Slide 27
3-Level Adaptive Differencing
PENTRAN has 3 adaptive differencing levels
  All schemes based on 0th spatial moment balance
  Less parallel information to pass on a given mesh compared to higher order methods
  Level 1: Diamond Zero (DZ)
    Use DZ until a fixup is needed
  Level 2: Directional Theta-Weighted (DTW)
    Use until weight exceeds 0.95 (Petrovic and Haghighat)
  Level 3: Exponential Directional-Iterative (EDI)
    Intended for severe streaming (Sjoden; Sjoden and Haghighat)

## Slide 28
Level 1: DZ
Diamond Zero (DZ) Differencing
  Still main scheme in many production codes
  Simple, fast, linear flux extrapolation
  Good in source regions/slowly varying flux
  Non-linear “zero fixup” when exiting flux < 0
  Prone to unphysical solution oscillations
  Very ill-conditioned for parallel processing

## Slide 29
Directional Theta Weighted Differencing
  evolution from TW scheme (Rhoades & Engle) to a directional weighting by Petrovic and Haghighat
  positive, with "proper” stable flux behavior
  eliminates inherent oscillations
  excellent in general, costs ~10%>DZ in 3-D
  inaccurate with severe streaming, larger cells
    equivalent to step scheme when cells are thick
Level 2: DTW

## Slide 30
Level 3: EDI
Exponential Directional Iterative Differencing
  DTW predictor provides l coefficient guess for auxiliary
  Grew from EDW scheme
  EDI formulation corrects average, outgoing flux
  Still a 0th order based (spatial moment) scheme
  Inherent positivity, accuracy in severe streaming
  Cost: up to 2x DTW in 3-D, depending on l coeff iterations

## Slide 31
Consider auxiliary partial derivatives
Applying the balance equation along x yields
Fixed point iteration formulations
Costs ~40%>DZ
Level 3: EDI

## Slide 32
EDI: NSE Vol 155, pp. 179-189 (Feb 2007)
32

## Slide 33
Non-Upgraded Schemes
Scheme 4: EDW Scheme
  Similar to EDI scheme, but exponential arguments fixed at initial guess from DTW without iteration
  Not typically as accurate as EDI, but can be a compromise between speed and accuracy when regions are known to require exponential treatment
  Is not part of the 1-2-3 adaptive differencing sequence and must be selected by the user

## Slide 34
Non-Upgraded Schemes
Scheme 5: CRT Scheme (Developed by Yi and Haghighat)
  Characteristic Ray Trace (CRT) is a block-oriented transport solution method adapted for a coarse-mesh where the transport is solved along a characteristic ray projected across the coarse mesh coupled in flow to surrounding Sn meshes
  Each set of characteristic rays are parallel to a direction of the angular quadrature from Sn.
  Considers the whole coarse mesh as one region
    The cross-section and angular source terms are constant throughout the region
  CRT is not allowed for CMs containing fission or independent sources
  Still main scheme in many production codes
  Simple, fast, linear flux extrapolation
  Good in source regions/slowly varying flux
  Non-linear “zero fixup” when exiting flux < 0
  Prone to unphysical solution oscillations
  Very ill-conditioned for parallel processing

## Slide 35
3-Level Adaptive Differencing: Selective Upgrade/Tuning Feature
  Level 1 → Level 2 : DZ to DTW Upgrade
    Use DZ until a fixup is needed
  Level 2 → Level 3 : DTW to EDI Upgrade
    Use until DTW weight exceeds 0.95 (weights close to 1 indicate ‘step’ differencing)
      Strategy effective for no or low-level source
      For strong sources, a test is performed with ‘qfratio’
        If qfratio > 1.00 (default), DTW persists and we do not upgrade
    No upgrade is performed if optical thickness of cells is less than 0.02 – for ‘vanishingly thin cells’ – stay with DTW

## Slide 36
Numerical Testing: Simple Slab

## Slide 37
Uses a higher order mesh coupling scheme: Taylor Projection Mesh Coupling (TPMC)
Accelerations…
  Two-grid 3-D TPMC-coupled “/” multi-grid transport acceleration
  PCR with a zoned rebalance acceleration
  Preconditioning with REPRO
    Use a previous model to accelerate computation
Multigroup & One-level SI schemes
Other Numerical Treatments

## Slide 38
Coupling of Discontinuous grid densities
  Allow high definition in ROIs, parallel load balance
First Order Taylor projection of angular fluxes at interface between discontinuous grid surfaces
  Flow Step
  Particle Balance Step
  Important for “Coarse to Fine”
Taylor Projection Mesh Coupling

## Slide 39
Allows for automatic Red-Black or Block-Jacobi, Automatic load balancing
Anisotropic scattering, arbitrary Pn moments
3-D angular quadratures
  level symmetric through S20, Legendre-Chebychev (Pn-Tn), arbitrary order
Vacuum, reflective, group-albedo boundaries
Volumetric sources, plane surface fluxes, currents
PENDATA, other utilities…
More Features

## Slide 40
Demonstrated 97% to 98% parallel fraction
  Performance depends on problem, decomposition
  Development focus on high accuracy & parallel efficiency
  Numerous applications over the past 14 years
Speedups of 50-nx100 are achievable
  Demonstrated scalability
  http://www.hswtech.com/pdfs/PENTRANmanual.pdf
PENTRAN

## Slide 41
Simple Example: hello.f

## Slide 42
Venus-3 Model
PENMSH-XP code used to generate 3-D Cartesian Grid
~85,000 cells
26 Groups
P3-S8 Discrete Ordinates
Group 1 Flux Solution:

## Slide 43
Compared 370 Measured Rxn Rates (Ni, In, Al dosimeters)
vs Integral Rxn Rates computed from PENTRAN P3-S8 26 group-dependent fluxes.
95% C/E values +/-10%; 5% within +/-15% (near P/L rods).
Venus-3 Results

## Slide 44: BWR Core Shroud Problem
BWR reactor and Core Shroud Assembly…
…with baffles, jet pumps, steam voids, etc.
(Top) 67 Group P3-S8 coupled neutron-gamma calculation
265,264 fine mesh cells
Solved in 12 hours on 48 IBM-SP2 processors… 8 processors angular, 6 processors spatial decomposition.

## Slide 45: BWR Core Shroud Results
Displacement per Atom (DPA) in the core shroud shows intense radiation damage where fuel is close to the shroud.
Results were verified independently by Monte Carlo computations
Multigroup PENTRAN (using BUGLE-96) values were within 5-15% of continuous energy MCNP values.
(Kucukboyaci, et. al, 2000).

## Slide 46
X-Ray Modeling ...
90 m3 room discretized into ~131,000 3-D cells
PENMSHTM code (8 “z-levels” floor to ceiling)
BUGLE-96: last 4-group photon xsecs
80kV radiographic W-anode 32 mAs x-ray burst
  Rotating anode water cooled
Hybrid X-ray Spectrum
  Characteristic X-rays
  Bremsstrahlung continuum

## Slide 47
X-Ray Dose, z=100 cm

## Slide 48: Gamma Transport Example
        0.5 MeV 0.5 MeV
        forward adjoint
        (relative to
        detector response)
        0.15 MeV 0 0.15 MeV
        forward adjoint

## Slide 49: “TIEL” Benchmarks Tested the Numerics…
Proposed by Ganapol
  Ganapol, JBC-M&C Division, 2006, Source Series I
Goal: provide a set of analytical benchmark problems, solutions
  infinite media, Variety of sources
    Plane, Sphere, Shell, Point…
Well documented and solved using quasi-analytic methods
  Fourier Transform inversion
  Henyey-Greenstein (H-G) scattering kernel σl=c g l , Up to L=24 Scattering Order
Advantages
  Can be unequivocally used as standards of comparison
  Enable direct assessment of the quality of solutions and methodologies

## Slide 50: Planar Source Problem
Difficulties close in near source (also noted by Ganapol) , accuracy affected by extent of the boundary in the model ->
Scalar flux solution at x=0.01 mfp (close in) for the plane source:
  Effect of the SN order for c =0.9, g =0.9, L=12, ε=10-3
  Up to S64 (4224 directions/mesh)
x (mfp) | PENTRAN-S34 | Ref[1] | Rel_diff (%)
0.01 | 3.05371 | 3.29089 | 7.20718
1.12 | 0.9458 | 0.94499 | -0.08529
2.23 | 0.62624 | 0.62603 | -0.03353
3.34 | 0.45239 | 0.45228 | -0.02454
4.45 | 0.33914 | 0.33908 | -0.01698
5.56 | 0.25937 | 0.25937 | -0.00001
6.67 | 0.20073 | 0.20081 | 0.03984
7.78 | 0.15651 | 0.15671 | 0.13081
8.89 | 0.12256 | 0.12295 | 0.31233
10.00 | 0.09618 | 0.09681 | 0.65125

## Slide 51: Point Source
The most challenging problem for a 3-D code
Isotropic source in a highly anisotropic medium
  Modeled as a 12 x 12 x 12 mfp box divided in 86,000 fine cells of 5 mm (each side) cells, except for center region (0.5 mm)
  First coarse mesh: Source (origin) as one single fine mesh cell of 0.5 mm size

## Slide 52: PENTRAN Solution Summary
Scalar flux solutions for the 1-D sources: c=0.9, g=0.9, L=12

## Slide 53: TIEL Benchmark Findings
PENTRAN demonstrated Good Agreement with benchmarks
  Solutions accurate to < 0.7% difference
  Demonstrated accuracy and asymptotic convergence
Verified arbitrary SN PL formulations in code
  3-D Legendre-Chebychev quadratures to N=64 (4224 dir) here
  3-D Anisotropic scattering to L=24
Other Issues
  EDI vs EDW differencing algorithms; EDI better adapts to various scattering situations
  Verified Angular-Spatial Parallel numerics of PENTRAN
    Importance of parallel computing to yield results in 3-D codes
  Excellent learning exercise for students
  Confidence in solutions as we develop other supporting tools & methods

## Slide 54: Simplified Co-60 Problem
Idealized model of a teletherapy device for benchmark applications
This model consisted of four key components:
source (2×2×2 cm3)
lead source housing 4 cm thick, air layer
homogeneous water phantom (30×30×30 cm3)
P3-S42 Discrete Ordinates (1848 directions/ mesh/energy group)

## Slide 55: Investigation of Angular Quadrature

## Slide 56: OSU Reactor Model

## Slide 57: PENBURN with ‘BURNDRIVER’ methodology
“Forward-Euler” approach - fluxes solved at the beginning of each time step are assumed to be constant over step.
  Considerations are currently being made to consider a mid-step depletion/transport calculation to forecast mid-step fluxes.
Infinite dilution cross-section treatment – microscopic cross sections are assumed to remain constant through burnup.
  Dehart has shown this assumption begins to fail when in-growth reaches 1x10-3 atom/bn-cm.
  Cross-section updates need to be considered when reaching this large of in-growth.

## Slide 58
GMIX
Macro cross section mixer
PENTRAN
3-D Transport Solver
PENPOW
Reaction Rate Solver
PENBURN
Fuel Depletion Solver
Remix cross-sections based on new isotopic concentrations
REPRO
Flux preconditioner
for (n+1)burn step
prbname.f90
prbnames0.gmx
prbname.grp
burnset.inp
prbnames(n+1).gmx
GETDATA.sh
KEFF.sh
stepn
folder
Finish all burn steps?
prbname.xsc
penburn.path
burnsum.out
keff.out
burndriver.sh
Input
Output

## Slide 59: PENTRAN Westinghouse Assembly Calculation
Full length, 17x17 PWR assembly (w/out control rod fingerlings) is currently modeled in PENTRAN.
  Active length: 365.76 cm
  Assembly pitch: 21.5 cm
  Total PENTRAN meshes: 4.5 x 106
Homogenized fuel pins (fuel/gap/clad).
Each fuel pin modeled as unique material
  3*264 fuel materials + 1 water material = 793 total
  Allows for pin-by-pin depletion in PENBURN

## Slide 60: Westinghouse Assembly Model
Group 3
(E < 0.625 eV)

## Slide 61
Group 1
(1 MeV < E < 20 MeV)
Group 2 (0.625 eV<E<1 MeV)
Group 3
(E < 0.625 eV)

## Slide 62: SFCOMPO Database
SFCOMPO: Spent Fuel COMPosition Database
  Found at http://www.nea.fr/sfcompo/
Database which archives isotopic compositions of spent fuel assemblies pulled from power reactors.
Determined from gamma spectrometry and chemical analysis.
Originally developed by the JAERI Department of Fuel Cycle Safety Research's Fuel Cycle Safety Evaluation Laboratory and later transferred to the NEA.

## Slide 63: SFCOMPO (cont’d)
Contains data for PWR and BWRs from Germany, Italy, and Japan.
Provides operation history for fuel element, and even shows position in core at each irradiation step.
Website includes search engine which allow the user to search based on a reactor name or range of burnup, initial enrichment, and cooling time after irradiation.
Good alternative to comparisons with SCALE simulations.

## Slide 64: Investigation of Mesh Interval
Mesh variations in the Co-60 model

## Slide 65: Co-60 Device 3-D scalar flux distributions slices model at different x-levels with S12
gamma-ray 3-D Group 1 scalar flux distribution for depth 0cm, 5cm, 10 cm and 15 cm, computed by PENTRAN with the BUGLE-96 gamma cross section library, (An S12 angular quadrature,168 directions, with P3 scattering anisotropy was used).

## Slide 66
Gamma-ray 3-D Group 1 scalar flux distribution for x-level depths at 0cm, 5cm, 10 cm and 15 cm, computed by PENTRAN with the BUGLE-96 gamma cross section library; an S42 angular quadrature (1848 directions) with P3 scattering anisotropy as a reference case.
Co-60 Device 3-D scalar flux distributions slices model at different x-levels with S42

## Slide 67
Significant efforts in
Shielding calculations…

## Slide 68: BURNDRIVER
PENBURN sequence is now automated with the release of BURNDRIVER shell script.
Script creates all necessary directories, moves inputs/outputs, executes programs, and creates output summary files.
Requires 6 input files:
    1. burnset.inp 2. prbname.gmx
    3. penburn.path 4. prbname.xsc
    5. prbname.f90 6. prbname.grp
PENMSHXP
PENTRAN geometry/input generator
SCALE5.1
T-NEWT
Micro cross-section generator
prbname.xsc
prbname.f90
prbnames0.gmx
prbname.grp
penburn.path
burnset.inp
DEV-XS
GMIXFORM and COLLAPSEFORM
Sources of input files.
SCALFORM

## Slide 69: burnset.inp
/ problem name
whpin
/ # of processors for parallel PENTRAN run
8
/ Following 3 lines dedicated to PENPOW Problem Description
Westinghouse Hetr Pin Burnup Study
17 x 17 OFA Assembly
Fuel Gap Clad Moderator Regions
/ number of fuel materials, no. nonburn nuclides
1
/ range of fuel material number: eg. 1 10
1 1
.
.
.

## Slide 70: burnset.inp
*Very familiar to penburn.inp
/ Following 3 lines dedicated to PENBURN Problem Description
Westinghouse Hetr Pin Burnup Study
17 x 17 OFA Assembly
Fuel Gap Clad Moderator Regions
/ # of irradiation/cool steps
2
/ power, time, time unit (d), irrad (i)/cool(c), print step, print option, GMIX keyword
-30 1 d i 1 2 s1
-30 3 d i 1 2 s2

## Slide 71: INTERP-XS
Purpose: Creates a problem dependent microscopic cross-section file based on specified:
  Avg. system energy (MeV)
  Operating temperature (K)
  Burnup (GWd/MTU)
Microscopic cross-section libraries generated for three reactor systems:
  Thermal: PWR WH fuel pin
  Epithermal: Graphite moderated Magnox fuel pin
            Loosely based off of UFCD II design
  Fast: Clinch River Breeder Reactor fuel pin
            Hexagonal lattice, Na cooled
  NOTE: Spectra characterized by MCNP analysis of unit cell’s neutron density distribution.

## Slide 72: INTERP-XS (cont’d)
System temperatures: 300, 650, 1000, 1350 K
Libraries currently exist for fresh fuel concentrations
    Libraries for mid-cycle fuel compositions are work in progress.
2 types of interpolation methods:
  Linear interpolation
    Option for using lethargy, ln(Eo/E), instead of energy, E
  Aitken’s Method: work in progress